## Slide 1: OEG results in the IoT domain
Ontology Engineering Group
Universidad Politécnica de Madrid

## Slide 2: Semantic interoperability in the IoT
IoT value creation requires collaboration
between networks of cross-domain devices and services
Data
Content
Context
Physical
time, location, etc.
Application
tasks, goals, etc.
Ontologies
Express shared meaning
Ensure consistency
Need open standards!
Interoperability
Discovery
Exchange
Understanding

## Slide 3: Overview of the W3C Semantic Sensor Network ontology
SSO Pattern
Device
Deployment
PlatformSite
System
System
onPlatform only
hasSubsystem only, some
SurvivalRange
hasSurvivalRange only
OperatingRange
hasOperatingRange only
hasDeployment only
DeploymentRelatedProcess
Deployment
deploymentProcesPart only
deployedSystem only
Platform
deployedOnPlatform only
attachedSystem only
Device
Sensor
SensingDevice
Sensing
implements some
observes only
hasMeasurementCapability only
inDeployment only
Stimulus
detects only
isProxyFor only
ObservationValue
SensorOutput
hasValue some
isProducedBy some
Process
Process
hasInput only
hasOutput only, some
Input
Output
Observation
observedBy only
featureOfInterest only
observationResult only
Property
observedProperty only
hasProperty only, some
isPropertyOf some
sensingMethodUsed only
includesEvent some
FeatureOfInterest
ConstraintBlock
Condition
inCondition only
MeasuringCapability
MeasurementCapability
forProperty only
OperatingRestriction
inCondition only
Data

## Slide 4: Sensor capabilities example
Sensor
observes
hasMeasurementCapability
ObservationValue
Property
MeasurementCapability
forProperty
MeasurementProperty
hasMeasurementProperty
MeasurementRange
hasQuantityValue
hasQuantityUnitOfMeasure
hasMeasurementPropertyMinValue
hasMeasurementPropertyMaxValue
Sensor001
cd:WaveHeight
WaveHeightMeasurementCapability
WaveHeightMeasurementRange_1
WaveHeightValue_1
3.6
hasQuantityValue
WaveHeightValue_2
meter
1.2
hasQuantityUnitOfMeasure
dul:UnitOfMeasure
“Sensor001 can measure wave heights with a minimum value of 1.2 and a maximum one of 3.6”

## Slide 5: Sensor data example
Location | Zone | Sensor | Air quality
... |  |  | 
La Vaguada | Hall floor 1 | Air sensor 007 | 3
La Vaguada | Stairs floor 1 | Air sensor 008 | 4
La Vaguada | Hall floor 2 | Air sensor 009 | 4
... |  |  | 
Location
includesElement
FeatureOfInterest
LaVaguada
HallFloor1
Property
AirQuality
hasProperty
Observation
Observation0844
featureOfInterest
observedProperty
SensorOutput
Output37832
observationResult
Sensor
AirSensor007
isProducedBy
hasValue
“3”^^xsd:int
observes

## Slide 6: Web of Things ontology
Aligned with the W3C Web of Things IG

## Slide 7: Web of Things example
“LED Lamp (Thing) that supports multiple protocols (CoAP and HTTP), mediaTypes (JSON and EXI), and security policies (it requires a JWT for interaction). It also shows the definition of the endpoint information in a global manner.”

## Slide 8: Web of Things prototype - City Light Pollution
Architecture – Integrating photometer streams and DBpedia
Photometers measure…
Sky & ambient temperature
Sky brightness
Position (lat, long)

## Slide 9: Access to distributed (WoT) Linked Data
Agora SPARQL interface – What is the average sky temperature in Madrid right now?
SELECT (AVG(?tsky as ?avg) WHERE {
{
?w wot:offersInteraction [
rdfs:label “lat”;
wot:hasLatestEntry [
wot:value ?tlat
]
] .
?w wot:offersInteraction [
rdfs:label “long”;
wot:hasLatestEntry [
wot:value ?tlong
]
] .
?w wot:offersInteraction [
rdfs:label “tsky”;
wot:hasLatestEntry [
wot:value ?tsky
]
] .
}
{
[] a sch:Place ;
foaf:name ?name ;
geo:lat ?lat ;
geo:long ?long
}
FILTER(STR(?name)=“Madrid” && (?tlong-?long)*(?long-?tlong) < 1 && (?tlat-?lat)*(?lat-?tlat) < 1)
}

## Slide 10: Projects and initiatives
2008
2016
SSN XG 2009
SDW WG 2015
SAREF 2016
2010
Data streams
Ontology development

## Slide 11: Results
SSN XG
SDW WG
SAREF
Sensor data representation. W3C incubator group
Sensor data representation. W3C working group
Smart appliances data representation. Extensions for environment and buildings. ETSI STF
Ontology-based access to streaming data sources
Sensor networks and sensor data representation
IoT infrastructure and IoT data representation
APIs for IoT data
Ontology-based access to streaming data sources
SPARQL-based access to streaming data